## Slide 1
AstroNex
PROPOSED SOLUTION
Foveated 2.5D LiDAR mapping for autonomous ground vehicles
THE PROBLEM
3D point clouds are too heavy for real time. Flat 2D grids lose kerbs, ditches and overhangs.
OUR SOLUTION
Drishti-2.5 turns every raw LiDAR scan into a compact, labelled 2.5D terrain map - sharp near the vehicle, lighter far away.
RAW LIDAR SCAN
~124k 3D points every scan
DRISHTI-2.5
1 Find the ground
2 Label every point
3 Build the adaptive grid
4 Group obstacles
2.5D MAP OUTPUT
5 cm cells
to 10 m
10 cm cells
to 25 m
50 cm cells
to 100 m
Height + class in every cell · not to scale
Ground Separation
Separates ground from everything above it, so terrain height is correct.
Patchwork++
Point-Level Labels
Labels each laser point as road, vehicle, person, pole or 15 other classes.
FRNet · 19 classes
Foveated 2.5D Grid
Uses fine 5 cm cells near the vehicle, growing to 50 cm at 100 m.
Integer ring lattice
Obstacle Evidence
Groups labelled points into obstacles; tracks vehicles and people over time.
Candidates + track IDs
What makes it different: every point lands in exactly one cell - no gaps or double counts at ring edges. Unknown stays unknown, never silently marked safe.
SMART INDIA HACKATHON 2026 · SIH26053
2
Notes: PROPOSED SOLUTION - speaker notes Main message: Drishti-2.5 turns each raw LiDAR scan into a compact, labelled 2.5D terrain map, sharp near the vehicle and lighter far away. Say: "A LiDAR gives about 124 thousand 3D points every scan. That is too heavy to process at full detail, but flattening it into a 2D grid throws away the heights that reveal kerbs and ditches. Drishti-2.5 takes the middle path the problem statement asks for: a 2.5D map that keeps height and class in every cell, with 5 centimetre cells close to the vehicle and 50 centimetre cells out to 100 metres, like human foveated vision. It separates ground, labels every point with a deep network, builds the adaptive grid and groups obstacles. Two design rules matter: every point goes to exactly one cell, so nothing is lost or double counted where rings meet, and anything the system is unsure about stays marked unknown." Evidence - Problem and suggested 5 cm / 10 m and 50 cm / 100 m cells: SIH26053 problem statement (DRDO). - ~124k points per scan: measured mean 123,558 accepted points over 20 SemanticKITTI sequence 08 scans (docs/research/experiments/0031-adaptive-vs-uniform-grid.md). - Rings 5/10/50 cm to 10/25/100 m: Drishti-2.5/configs/default.toml. - Exactly-one-cell ownership, unknown never turned into a class: Drishti-2.5 contracts (docs/interfaces.md) and unit tests (87 passed, docs/testing.md). - Obstacle candidates and track IDs: experiments 0028 and 0030. Velocity is not estimated.

## Slide 2
AstroNex
TECHNICAL APPROACH
One pipeline: raw scan in → labelled 2.5D map out
IN
PROCESS
OUT
1
Scan Input
Reads each scan with time and pose; rejects invalid points.
64-beam LiDAR replay · ROS 2 proposed
2
Ground Segmentation
Fits local ground patches to split ground from everything above.
Patchwork++ · IROS 2022
3
Semantic Labels
Deep network gives each point one of 19 classes; unknown kept.
FRNet · IEEE TIP 2025
4
Adaptive 2.5D Grid
Places every point in exactly one ring cell by integer index.
5 / 10 / 50 cm rings
5
Obstacle Evidence
Clusters labelled points; keeps vehicle and person IDs across frames.
Candidates + track IDs
6
Map & Dashboard
Publishes a read-only map, audit record and colour-coded 3D view.
Map snapshot · Rerun
WHAT EACH 2.5D CELL STORES
ground height
obstacle
height span
one cell
Ground height
Obstacle height span
Class evidence (19)
Point count
Intensity
Ambiguity flag
Heights in integer centimetres. Every accepted point is counted once.
COMPUTE TODAY
Laptop CPU · fully offline · no cloud
MEASURED
Geometry path: median 83 ms per scan over 1,000 scans.
MEASURED
FRNet on CPU: ~7.2 s per scan, so a GPU is required.
PROPOSED
NVIDIA GPU path (coded, not yet validated) and ROS 2 live input.
Proven / Measured
Proposed
Test / Validate
SMART INDIA HACKATHON 2026 · SIH26053
3
Notes: TECHNICAL APPROACH - speaker notes Main message: one shared pipeline carries a raw scan to a labelled 2.5D map and obstacle evidence, and every stage is already running and measured. Say: "A scan comes in with its timestamp and pose, and invalid points are rejected. Patchwork++, a published ground-segmentation method, splits ground from everything above it. FRNet, a published LiDAR segmentation network, labels every point with one of 19 classes; anything it cannot classify stays unknown. The adaptive grid then puts every point into exactly one cell using integer indices, so rings never overlap. Labelled points are grouped into obstacles, and vehicles and people keep an ID across frames. Out comes a read-only map snapshot and a colour-coded 3D view. Everything runs offline on a laptop CPU today. The geometry path takes a median 83 milliseconds per scan; the neural network takes about 7 seconds on CPU, so real-time use needs a GPU. We have coded a GPU path but not yet validated it on NVIDIA hardware." Evidence - Patchwork++: Lee, Lim, Myung, IROS 2022, https://arxiv.org/abs/2207.11919 ; code https://github.com/url-kaist/patchwork-plusplus - FRNet: IEEE Transactions on Image Processing 2025, Apache-2.0 code and SemanticKITTI weights, https://github.com/Xiangxu-0103/FRNet ; checkpoint pinned by SHA-256 (experiment 0025). - Cell fields: Drishti-2.5/src/drishti/mapping.py (MapSnapshot). - Geometry path median 83.13 ms over 1,000 sequence 08 scans, geometric mode without the model (E-044, experiment 0019). 28 of 1,000 scans exceeded 100 ms. - FRNet CPU p50 7,177 ms per scan (E-052, experiment 0026). - CUDA path integrated with no GPU parity or timing result (docs/open-items.md, O-001). - ROS 2 PointCloud2 carries point fields, timestamp and frame ID: https://raw.githubusercontent.com/ros2/common_interfaces/rolling/sensor_msgs/msg/PointCloud2.msg

## Slide 3
AstroNex
FEASIBILITY AND VIABILITY
Working replay prototype. A staged path to field deployment.
Technical Feasibility
Every stage already runs end to end on real LiDAR data.
PROVEN
Patchwork++ and FRNet are published, open and integrated.
67.55%
mIoU on 4,071 held-out scans (authors report 68.7%)
Operational Feasibility
Runs fully offline on the vehicle's own computer.
PROVEN
No cloud or network needed at runtime.
TEST
Dust, rain, off-road terrain, live sensor, calibration.
69.1%
mIoU within 20 m; 15.7% beyond 50 m
Economic Viability
Prototype needs a laptop and open software, not new rigs.
PROVEN
Open-source stack, public data, no paid APIs.
VALIDATE
Vehicle GPU cost; dataset and model licences.
33.6%
smaller per-scan map than uniform 5 cm (measured)
Scalability
Rings, radii and sensors change by config, not code.
PROVEN
Grid rings set in a validated config file.
PROPOSED
ROS 2 adapter for other LiDARs; GPU path.
~31×
fewer cells than uniform 5 cm at full 100 m (calculated)
Long-Term Viability
Every result is pinned, hashed and repeatable.
PROVEN
87 automated tests, locked dependencies, checkpoint SHA-256.
PROPOSED
Regression gates and named maintainers per release.
Path to Field
Prototype Real-data replay, all stages
DONE
Validation Held-out metrics, GPU timing
WE ARE HERE
Field Trial Live sensor, terrain, weather
NEXT
Deployment Vehicle integration via ROS 2
LATER
Defence Fit
DRDO VRDE lists AI-based perception and AI-algorithm validation among UGV technology tasks.
Relevance only, not endorsement.
Proven / Measured
Proposed
Test / Validate
SMART INDIA HACKATHON 2026 · SIH26053
4
Notes: FEASIBILITY AND VIABILITY - speaker notes Main message: the prototype already runs on real data with open tools; the remaining steps to the field are named, measurable and in order. Say: "Is it practical? Technically, yes: every stage runs end to end on real LiDAR data today. On all 4,071 scans of the standard held-out sequence, the labelling scores 67.55 percent mIoU, close to the 68.7 percent the FRNet authors report. Operationally, it needs no network. It is strongest near the vehicle, 69 percent within 20 metres, and weak beyond 50 metres, which is why the grid is coarse there and why field trials come next. Economically, the prototype needs only a laptop and open software, and the adaptive grid stored 33.6 percent less map data per scan than a uniform 5 centimetre grid. Ring sizes and sensors are configuration, and every result is hashed and repeatable. We are between prototype and validation. The next gates are GPU timing, live sensor input and field trials in dust, rain and rough terrain." Evidence - 67.55% mIoU (0.6754690443) and 92.28% labelled accuracy, 4,071 sequence 08 scans, official evaluator (E-051, experiment 0025). The run joins a 793-scan prefix and a 3,278-scan continuation. - FRNet authors report 68.7% SemanticKITTI validation mIoU under their conditions: https://github.com/Xiangxu-0103/FRNet - Sequence 08 is the official validation split: semantic-kitti-api config/semantic-kitti.yaml, https://github.com/PRBonn/semantic-kitti-api - Range results 69.1% (0-20 m), 54.3% (20-50 m), 15.7% (50 m+): experiment 0025. - 33.6% fewer cells and snapshot bytes than uniform 5 cm, 20 scans, single frame, logical payload (E-058, experiment 0031). - ~31x fewer cells at full 100 m coverage is a design calculation (12,566,371 vs 408,407 cells), not a measurement. - SemanticKITTI is CC BY-NC-SA (non-commercial): https://semantic-kitti.org/dataset.html - 87 tests passed, locked uv.lock, checkpoint SHA-256: docs/testing.md, experiment 0025. - DRDO VRDE UGV tasks include "AI Based Perception for Autonomous Driving" and "Simulation software for AI algorithms validation": https://drdo.gov.in/drdo/en/offerings/technology-foresight/ugv (checked 2026-09-29).

## Slide 4
AstroNex
IMPACT AND BENEFITS
Economic
33.6% less map data per scan than a uniform 5 cm grid (measured).
Smaller maps suit lower-cost embedded computers (hardware to validate).
One reusable pipeline avoids rebuilding perception per platform.
Height evidence may reduce terrain-related vehicle damage (field trials needed).
Environmental
Less map data to store and process for every scan.
Lower compute load can reduce power draw (not yet measured).
Could extend battery operating time (to validate on a vehicle).
Runs offline: no cloud servers or data transfer.
Strategic / Indigenization
Team-owned pipeline Indian engineers can audit, retrain and extend.
Aligns with DRDO VRDE's listed AI perception and validation tasks.
Config-driven grid fits many vehicle platforms (ROS 2 adapter proposed).
Dual-use: defence UGVs and civilian autonomous mobility.
Field Operators & Reconnaissance UGVs
5 cm cells within 10 m keep near-field height detail where kerbs, mounds and trenches appear.
Colour-coded map with flagged uncertain cells supports operator awareness in rough terrain (field trials needed).
Robotics Researchers & Students
No need to rebuild mapping and evaluation code for each experiment.
Reusable mapping core with hashed runs and official scoring supports adaptive perception, semantic mapping and navigation research.
Civilian Autonomous Mobility
Road vehicles meet potholes, pedestrians and unexpected obstacles.
Tested on real urban driving scans: labels people, vehicles and poles, with height per cell.
Adaptive detail lowers map data, which may make perception more affordable (cost not estimated).
Benefits describe mechanisms already built. Items in italics, and field outcomes such as safety and mission time, still need validation.
SMART INDIA HACKATHON 2026 · SIH26053
5
Notes: IMPACT AND BENEFITS - speaker notes Main message: if Drishti-2.5 works in the field, six groups gain: lower cost and compute, lower energy use, indigenous capability, field operators, researchers and civilian mobility. Say: "What changes if this works? Economically, the adaptive grid already stores 33.6 percent less map data per scan than a uniform 5 centimetre grid, which points toward cheaper embedded computers, though we still have to validate that on hardware. Less compute can also mean less power and longer battery life; we have not measured that yet, and the slide says so in italics. Strategically, it is a team-owned pipeline that Indian engineers can audit and retrain, aligned with the AI perception and validation tasks DRDO's VRDE lists for unmanned ground vehicles. For field operators, 5 centimetre cells near the vehicle keep the height detail where kerbs, mounds and trenches appear, and uncertain cells are flagged rather than shown as safe. Researchers get a reusable mapping core with repeatable, hashed evaluation. And the same approach applies to civilian vehicles: we have tested it on real urban driving scans. Anything in italics still needs field or hardware validation." Evidence - 33.6% less map data per scan: E-058, docs/research/experiments/0031-adaptive-vs-uniform-grid.md (20 sequence 08 scans, single-frame logical payload). - 5 cm cells within 10 m: Drishti-2.5/configs/default.toml. - Per-cell ground height, obstacle height span, class evidence and ambiguity flags: Drishti-2.5/src/drishti/mapping.py. - Runs offline with local models: Drishti-2.5/src/drishti/learned.py; E-052. - Hashed runs and official scoring: experiment 0025 (checkpoint SHA-256, pinned official SemanticKITTI evaluator). - Urban driving data: SemanticKITTI is built on KITTI odometry driving sequences, https://semantic-kitti.org/dataset.html - VRDE UGV tasks "AI Based Perception for Autonomous Driving" and "Simulation software for AI algorithms validation": https://drdo.gov.in/drdo/en/offerings/technology-foresight/ugv - NOT measured: power draw, battery time, embedded hardware cost, vehicle damage, operator workload, mine detection. Mines are deliberately not claimed.